## Slide 1
SS2000
GSM/GPRS Baseband SoC - Memory Architecture
v7.1 - Final architecture · Cache + banked OCM + dedicated TCM
Application Core (Core 0)
32 KB I$ + 16 KB D$
RV32 + P-ext · L2/L3, MMI, AT, audio framework · runs from PSRAM
DSP Core (Core 1)
24 KB cache + 256 KB OCM + 36 KB TCM
RV32 + P-ext · 700 MHz · OCM banked 8×32 KB · TCM holds DFE + audio
Inter-core IPC
5 KB uncached carve-out in OCM
IPC 4 KB + GP ADC/DAC 1 KB · APB doorbell for IRQ
External memories
4 MB PSRAM + 4 MB Flash
PSRAM 200 cy · Flash 1600 cy @ 700 MHz · single-bank FOTA
Total on-die SRAM: 364 KB · Sampige Semiconductors · SS2000 Confidential · May 2026

## Slide 2
SS2000 System Memory Architecture
Dual RV32 P-ext · Application Core cache+PSRAM · DSP Core cache+OCM+TCM · shared via uncached OCM carve-out
APPLICATION CORE (CORE 0)
RV32 + P-ext · L2/L3, MMI, AT, audio framework, RTOS
RV32GC + P-ext · 700 MHz
5-stage pipeline
I-Cache · 32 KB
4-way · 64B line · LRU
PSRAM-backed runtime
D-Cache · 16 KB
4-way · 64B line · WB
PSRAM heap, messages
Why cache (not TCM)
• Code 1.5-2 MB - too big for TCM, fits 4 MB PSRAM
• Soft real-time only (~ms response, no burst deadline)
• Hot 75-90 KB → 32 KB I$ gives ~98% hit, AMAT ~5 cy
• Cold/FOTA stays in flash; runtime in PSRAM
DSP CORE (CORE 1)
RV32 + P-ext · L1 PHY, voice codec, AEC, NS, FM, audio decode
RV32 + P-ext · 700 MHz (full speed)
Cache + OCM + TCM hybrid
Cache 16+8
I$ + D$ (KB)
line-lock capable
OCM 256 KB
banked 8 × 32 KB
5 KB IPC carve-out
TCM 36 KB
DFE-Rx/Tx + audio
hard real-time only
Why cache + OCM + TCM
• TCM gives 1-cy guaranteed for HW-paced DFE / audio buffers
• OCM 5-cy penalty hidden by cache for code + L1 .bss
• Banking + line-lock available if determinism tightens
• Full 700 MHz fmax (TCM small enough to be off critical path)
IPC: 5 KB uncached carve-out inside OCM
4 KB APP↔DSP + 1 KB GP ADC/DAC · APB doorbell IRQ
PSRAM 4 MB
Application Core runtime + bulk buffers
Flash 4 MB
Cold + FOTA + resources
System architecture
SS2000 Confidential · v7.1 · May 2026

## Slide 3
Why cache + OCM + TCM for DSP Core
Three memory tiers, each chosen for a specific access pattern
Cache (16+8 KB)
Performance amplifier
• Hides OCM 5-cy miss penalty
• AMAT = 1.18 cy at 16 KB I$ + 3% miss
• Line-lock available for L1 PHY hot loops
• Transparent to software
OCM (256 KB)
Bulk code + data
• Holds codec, L1 PHY .text/.rodata/.bss
• 8 × 32 KB banks, individually I/D-mappable
• DMA target for kernel staging from PSRAM
• 5 KB uncached carve-out for IPC
TCM (36 KB)
Hard real-time only
• DFE-Rx 16 KB + DFE-Tx 16 KB ping-pong
• Audio-MIC 0.3 KB + Audio-out 3.75 KB
• 1-cycle deterministic - cache miss not allowed
• On DSP-CPU private bus, not AXI
Three tiers · Each for a specific access pattern
SS2000 Confidential · v7.1 · May 2026

## Slide 4
Application Core cache sizing - AMAT analysis
I-cache 32 KB / D-cache 16 KB · PSRAM-resident runtime code
Flash miss
1,600 cy
~2.3 us @ 700 MHz
PSRAM miss
200 cy
~286 ns @ 700 MHz
I-cache hit
1 cy
single-cycle
Target AMAT
<= 5 cy
usable responsiveness
AMAT under different I-cache sizes (textbook ballparks - validate via cachegrind)
I$ size
Typical miss rate
AMAT vs flash
AMAT vs PSRAM
Verdict
16 KB
~3-4%
1 + 0.035 x 1600 = 57 cy
1 + 0.035 x 200 = 8 cy
Marginal
32 KB
~1.5-2%
1 + 0.020 x 1600 = 33 cy
1 + 0.020 x 200 = 5 cy
Sweet spot (recommended)
64 KB
~0.5-0.7%
1 + 0.007 x 1600 = 12 cy
1 + 0.007 x 200 = 2.4 cy
Better but 2x silicon
Decision
32 KB I-cache + 16 KB D-cache, 4-way SA, 64-byte line, write-back, LRU
Runtime code must execute from PSRAM (not flash). Boot ROM relocates active text from SPI-Flash to PSRAM; cold/FOTA stays in flash.
Application Core · Cache sizing rationale
SS2000 Confidential · v7.1 · May 2026

## Slide 5
DSP Core sizing detail
16 KB I$ + 8 KB D$ · 256 KB banked OCM · 36 KB dedicated TCM
DSP CORE memory layout
RV32 + P-ext
700 MHz (full speed)
Single-issue in-order
5-stage pipeline
Line-lock on D$ for L1 PHY
I-cache · 16 KB
4-way · 64B line
line-lock capable
D-cache · 8 KB
4-way · WB · 64B
transparent OCM access
OCM - banked 8 × 32 KB
256 KB
32 KB
32 KB
32 KB
32 KB
32 KB
32 KB
32 KB
32 KB
Each bank I or D mappable. Codec + L1 PHY cached. 5 KB uncached carve-out for IPC + GP ADC/DAC.
TCM · 36 KB
DFE-Rx
16 KB
DFE-Tx
16 KB
Audio
4 KB
DSP-CPU private · hard-RT
DSP Core cache sizing · AMAT vs OCM (5-cy penalty)
I$ size
Miss rate
AMAT
Verdict
8 KB
~6-8%
1.35 cy
Acceptable
16 KB
~3-4%
1.18 cy
Sweet spot (recommended)
32 KB
~1.5-2%
1.10 cy
Better, +16 KB silicon
Why 16 KB I$ is enough
OCM is only 5 cy away (vs 200 cy PSRAM). Working set ~50 KB/TDMA frame fits comfortably. AMAT 1.18 cy is essentially free. Larger cache adds silicon for no measurable gain.
DSP Core sizing · 16+8 KB cache, 256 KB OCM, 36 KB TCM
SS2000 Confidential · v7.1 · May 2026

## Slide 6
Real-time timing — why TCM matters
TDMA frame 4.615 ms · DFE 8x oversampled at 2.17 Msps · zero tolerance for buffer overrun
T0
DL RX
T1
Idle
T2
Idle
T3
UL TX
T4
Codec
T5
T6
Measure
T7
1 TDMA frame · 4.615 ms · 8 slots × 577 µs
DFE-Rx → TCM
• DFE delivers 8× oversampled IQ
• 156 sym × 8 × 4 B = 5 KB per burst
• Ping-pong → 16 KB TCM allocated
• Cache cannot serve - HW-paced writes
DSP → DFE-Tx → TCM
• GMSK modulator output 8× oversampled
• Burst formatter writes 5 KB
• Ping-pong → 16 KB TCM allocated
• DAC consumes deterministically
Audio I/O → TCM
• MIC: 320 B (8 kHz mono, 20 ms)
• OUT: 3.84 KB (48 kHz stereo, 20 ms)
• DSP reads/writes via ISR
• Total audio: 4 KB TCM
Why TCM, not OCM, for these 36 KB
DFE writes are hardware-paced at 2.17 Msps. A cache miss to OCM (5 cy) during a DFE write could be acceptable, but a bus contention or arbitration delay is not — we cannot afford the risk of dropped samples. TCM gives 1-cycle deterministic write with no bus arbitration. The audio buffers follow the same logic — ISR-paced, no slack.
Real-time timing · TCM justification
SS2000 Confidential · v7.1 · May 2026

## Slide 7
Compiler optimization policy
-Os + LTO=ON for DSP Core codec/L1 · -O3 OK for Application Core application
Codec
-O3 size
-O3 MHz
-Os size
-Os MHz
Size saved
MHz cost
NB-AMR (full)
211 KB
32
63 KB
49
-70%
+53%
GSM-HR
85 KB
49
51 KB
68
-40%
+39%
GSM-FR
42 KB
7
9 KB
7
-79%
0%
AEC + NS
60 KB
42
35 KB
46
-42%
+10%
JPEG Enc+Dec
167 KB
14
108 KB
17
-35%
+21%
WAV Decoder
9 KB
2
4 KB
2
-56%
0%
-Os + LTO ON for DSP Core
Compiler shrinks code 40-70% at +10-50% MHz. DSP Core budget has 500+ MHz slack at 700 MHz target.
-O3 OK for Application Core
Application has soft real-time, cache hides flash/PSRAM misses. Optimize for speed in MMI loops.
Per-mode codec policy
AMR/EFR has 8 negotiated modes. Only one active per call. Single-mode = ~50% of full-codec.
Decision
Build pipeline: -Os + LTO=ON for DSP Core codec / L1 / AEC / NS · -O3 for Application Core app · Lint rule to prevent accidental DSP Core -O3
Compiler policy
SS2000 Confidential · v7.1 · May 2026

## Slide 8
Measured L1 PHY + per-block memory allocations
GSM_L1memusage.xlsx (RV32 -O3) + system architect per-block spec
Block
Source
Code
Data
Total
Note
L1 PHY (-O3, measured)
GSM_L1memusage.xlsx
13.4 KB
44.6 KB
58 KB
MLSE equalizer dominant in .bss
Codec DM (per-mode)
-Os per Raghava
-
12 KB
12 KB
One AMR mode active per call
AEC + NS DM
Measured
-
18 KB
18 KB
Time-banked across TDMA frames
Shared scratch
Measured
-
10 KB
10 KB
-
DMA buffers + ISR stack
Estimated
-
14 KB
14 KB
General DMA + RTOS ISR
DFE-Rx HW->DSP
SPEC
-
16 KB
16 KB
In DSP-CPU TCM
DFE-Tx DSP->HW
SPEC
-
16 KB
16 KB
In DSP-CPU TCM
Audio-MIC->DSP
SPEC
-
320 B
0.3 KB
In DSP-CPU TCM
DSP->Audio-out
SPEC
-
3840 B
3.75 KB
48 kHz stereo, 20ms, double-buffered
IPC + GP ADC/DAC
SPEC
-
5 KB
5 KB
OCM uncached carve-out (on AXI)
DSP Core SRAM TOTAL
-
-
-
353 KB
OCM 256 + TCM 36 + cache 24 + IPC 5
Coverage: L1 measured · codec/AEC/NS projected at -Os · DFE + audio + IPC from system architect spec
L1 + per-block spec · DSP Core 353 KB total
SS2000 Confidential · v7.1 · May 2026

## Slide 9
Codec catalog at -Os / LTO=ON
From Raghava measurements on BL808 RV32
Module
Status
IMEM @-Os
DM tables
Working
Per-mode active
NB-AMR (full 8 modes)
Measured
63 KB
~20 KB
5 KB
~42 KB single mode
GSM-HR
Measured
51 KB
~10 KB
5 KB
no modes - 51 KB
GSM-FR
Measured
9 KB
2 KB
2 KB
single mode
GSM-EFR
Projected
~45 KB
~8 KB
5 KB
equivalent to AMR-12.2
MP3 Decoder
Projected
~30 KB
~6 KB
20 KB
single mode
AAC Decoder
Projected
~40 KB
~10 KB
28 KB
one of several profiles
WAV Decoder
Measured
4 KB
1 KB
2 KB
trivial
AEC + NS
Measured
35 KB
~5 KB
14 KB
AEC and NS in different frames
JPEG Enc+Dec
Measured
108 KB
9 KB
34 KB
runs in OCM, no banking needed
Shared scratch
Measured
-
-
10 KB
-
FM Receiver
Unknown
TBD
TBD
TBD
TBD - reserve 16 KB OCM
All codecs fit in 256 KB OCM
Largest codec (JPEG 108 KB) sits in OCM, served via cache. Voice + AEC + L1 + JPEG can coexist with margin. No tile-mode banking required.
Codec catalog
SS2000 Confidential · v7.1 · May 2026

## Slide 10
Reference architecture comparison
MT6261 · SC6531E · SC6533G vs SS2000
Parameter
MT6261
SC6531E
SC6533G
SS2000
Main CPU
ARM7EJ-S
ARM926EJ-S
XCPU (RDA RISC)
RV32 P-ext (Application Core)
Main CPU cache
-
8 KB I + 8 KB D
4 KB I + 4 KB D
32 KB I + 16 KB D
DSP
FD216
TeakLite
VoC (Bi-MAC)
RV32 P-ext (DSP Core, cache+OCM+TCM)
DSP cache
-
-
-
16 KB I$ + 8 KB D$
DSP code memory
7 × 32 KB PM banks
48 KB PRAM
32 KB IRAM
256 KB OCM (banked, AXI)
DSP data memory
DM + IR
42 KB XRAM + 24 KB YRAM
20+20 KB
36 KB TCM (DFE+audio) + OCM
DSP ROM
Compressed blobs
86 KB XROM + ROMs
BBROM 96 KB
None - all from flash
Inter-core IPC
MCU/DSP regs
Shared mem + arbiter
COM Registers
5 KB OCM carve-out + APB doorbell
External Flash
External SPI
External SPI
4 MB integrated
4 MB external SPI
External PSRAM
External SPI
External SPI
8 MB integrated
4 MB external SPI
Approach
Dual-MCU + DSP
Triple-MCU + DSP
Dual-MCU + VoC
Dual RV32 - DSP in software
Insight
SS2000 collapses MCU + DSP into one dual-RV32 SoC. DSP Core total 316 KB (cache 24 + OCM 256 + TCM 36) - comparable to SC6531E TeakLite PRAM+XRAM+YRAM (114 KB) + ARM9 cache + IRAM (32 KB) + IROM 88 KB ROMs.
Reference comparison
SS2000 Confidential · v7.1 · May 2026

## Slide 11
Assumptions and Risks — read before tape-out
Single-architecture v7.1 baseline · recoverability noted for each
Assumption
Risk
Mitigation / Recovery
Per-mode AMR overlay <= 42 KB after RV32 port
M
If single-mode > 42 KB, OCM has 256 KB - just bump allocation. No silicon change.
DFE 8x sized per spec (16 + 16 KB TCM)
L
Per system architect. If oversampling rate increases, +16-32 KB TCM per increment.
Audio-MIC 320 B fits GSM voice only
M
For BT-HFP / AMR-WB / stereo recording, bump to 640 B / 1280 B / 3840 B in TCM.
TCM 36 KB sufficient for DFE+audio
M
If more HW-paced buffers added (e.g., FM IF samples), bump TCM by macro-size increment.
FM receiver fits in 16 KB OCM reserve
H
No measurement. Likely needs 16-32 KB. OCM has banking flexibility to absorb.
16 KB I$ + 5 cy OCM miss → AMAT 1.18 cy
M
Textbook ballpark - validate via cachegrind on reference firmware (osmocom-bb or LAVA IL2801).
Build pipeline enforces -Os + LTO=ON for DSP Core
M
Easy CI mistake to fall back to -O3. Add lint check / make rule.
5 KB OCM IPC carve-out uncacheable in hardware
L
Modern AXI MPU/PMA supports per-region cacheability. Standard pattern.
Single-bank FOTA in 4 MB flash
L
Standard: download to PSRAM, verify, atomic swap. Reversion needs cold reboot.
Net exposure: 1 High (FM) + 4 Medium + 4 Low. Max recovery cost = 32-48 KB OCM bump + cachegrind validation if all M-risks hit. No silicon respin required for most.
Assumptions & Risks
SS2000 Confidential · v7.1 · May 2026

## Slide 12
SS2000 v7.1 final memory provisioning
Tape-out budget · single architecture · see Slide 11 for risks
Application Core I-cache
32 KB
4-way SA, 64B, WB, LRU
Application Core D-cache
16 KB
4-way SA, 64B, WB, LRU
DSP Core I+D cache
24 KB
16 KB I$ + 8 KB D$, line-lock
DSP Core TCM
36 KB
DFE 32 + audio 4 (private bus)
DSP Core OCM (banked)
256 KB
8 × 32 KB · I/D mappable · 5 KB IPC carve-out
PSRAM
4 MB
External SPI · 200 cy · Application Core runtime + bulk
Flash
4 MB
External SPI · 1600 cy · cold/FOTA/NV
On-die SRAM by role: Application Core caches 48 KB · DSP Core cache 24 KB · DSP Core OCM 256 KB · DSP Core TCM 36 KB = 364 KB total
External memory: 4 MB PSRAM + 4 MB Flash = 8 MB
DSP Core hybrid runs at full 700 MHz fmax · no TCM-induced clock penalty · cache+OCM gives flat code space, no banking overlay required
v7.1 architecture commit
· Cache + banked OCM + dedicated TCM committed as the SS2000 architecture (Option A retired)
· DSP Core fmax 700 MHz · no banking complexity · -O3 OK except for -Os mandate on codec/L1 for size discipline
· DFE-Rx/Tx + audio in private TCM (hard real-time) · everything else cached from OCM
Still to validate
FM receiver footprint · MP3 + AAC at -Os · per-mode AMR DM split · cachegrind on reference firmware · AXI MPU per-region cacheability
Final provisioning · v7.1 tape-out budget
SS2000 Confidential · v7.1 · May 2026

## Slide 13
Backup: SS2000 vs reference parts
SC6531E and SC6533G "writable" numbers exclude 100-300 KB of pre-burnt code/data ROM
Memory
SC6531E (TeakLite)
SC6533G (VoC + BCPU)
SS2000 (DSP Core)
Writable code (RAM)
48 KB PRAM
32 KB VoC IRAM
24 KB cache + 256 KB OCM
Writable data (RAM)
42 + 24 = 66 KB X/YRAM
40 KB VoC + 16 KB BBSRAM
36 KB TCM (DFE+audio) + OCM share
Code ROM
86 KB XROM + ~200 KB PROM
96 KB BBROM
0 KB
Data ROM
16 KB YROM
0 KB
0 KB
Caches (subsystem MCU)
ARM9 8 + 8 KB
BCPU 1 + 1 KB
Application Core 32 + 16 KB
TOTAL on-die for L1 + codec
~416 KB (RAM + ROM)
~186 KB (RAM + ROM)
316 KB DSP Core (all RAM)
Active DSP firmware in use
105 KB (LZMA blob measured)
~130 KB (BBROM + VoC)
~50 KB peak resident
Why SS2000 doesn't use code ROM
• Both reference parts burnt vocoder primitives, FFT, codebook tables, A5/1 into silicon ROM.
• That commits codec choice for chip life - no FOTA fixes, no new codec support.
• SS2000 chose all-RAM so codec / L1 are fully updatable. Price: ~50-100 KB more SRAM area.
• Per-mode + -Os + cache + OCM shrinks active resident set to ~50 KB at any TDMA frame.
Option spectrum (for reference - not currently chosen)
Option
DSP Core RAM
Code ROM
Notes
Current v7.1 (all RAM)
256 OCM + 36 TCM
0 KB ROM
FOTA-friendly
+ A5 + FFT to ROM
~230 + 36
27 KB ROM
Spec-frozen primitives
+ vocoder ROM
~206 + 36
50 KB ROM
Codec locked at tape-out
SC6531E-style heavy ROM
~160 + 36
95 KB ROM
Mask spin per codec change
Backup · SS2000 vs SC6531E / SC6533G
SS2000 Confidential · v7.1 · May 2026

## Slide 14
Revision history
Changes from v4 (March 2026, SC-1 era) through v7.1 (current)
Rev
Headline
Details
V4.0
Original SC-1 baseline (Mar 2026)
ARM/FD216 binary analysis · 5-bank TCM concept · 420+192 KB reco
V5.0
SS2000 rebrand · pastel palette
DSP Core/Application Core naming · inter-frame banking · I-TCM 192 KB · 8+8 MB ext
V6.0
-Os/LTO + per-mode codecs
NB-AMR 211→63 KB · per-mode AMR · I-TCM 120 KB · 4+4 MB ext
v6.1
Aggressive cuts + Option B + risks
I/D-TCM 104 KB · risk panel · Option B (cache+OCM) introduced
v6.2
Title slide rebalanced
Option A + B as equal headline cards
v6.3
Banked OCM · DFE 8x estimate
OCM 256 KB banked (8×32, I/D mappable) · D-TCM +24 KB DFE
v6.4
System architect spec applied
DFE 16+16 + audio 4 KB · 5 KB AXI SRAM · D-TCM 144 KB
v6.5
Audio-MIC risk
320 B GSM voice only · bump for HFP/WB/stereo
v6.6
Recommendation reframed
Silicon area NOT the differentiator - fmax+simplicity vs det+power
v6.7
DFE+audio are TCM not OCM
Option B adds dedicated 36 KB TCM beyond 256 KB OCM
v6.8
Revision history slide added
First version of this slide
v6.9
Merge AXI SRAM into OCM · TCM visual
5 KB uncached OCM carve-out replaces separate AXI SRAM in Option B
v7.1
v7.0 architecture commit + v7.1 core rename
v7.0: single architecture committed (Cache + banked OCM + TCM), 364 KB on-die, Option A retired. v7.1: cores renamed to Application Core (Core 0) + DSP Core (Core 1) throughout.
Revision history · v4 → v7.1
SS2000 Confidential · v7.1 · May 2026